## Slide 1
Python hyperbola fitting algorithm
Python hyperbola fitting algorithm for GPR B-scan depth estimation.
It does:
Generate synthetic hyperbola points
Add noise
Fit the hyperbola equation
Estimate:
  target depth
  target horizontal position
  wave velocity

## Slide 2
The algorithm uses this equation:
Then it finds the best values of:
by minimizing the difference between the measured B-scan hyperbola points and the mathematical hyperbola model.
“The algorithm fits the theoretical GPR hyperbola equation to the detected reflection curve in the B-scan. From the best-fitting curve, it estimates the target depth, lateral position, and wave velocity.”
This is the key upgrade from forward simulation to inverse depth estimation.

## Slide 3
Automatic depth estimation code
Automatic depth estimation code. It generates a synthetic B-scan, automatically detects the hyperbola peak points, fits the hyperbola, and estimates depth
How this works
The code does four main things:
Generates a B-scan for a buried target.
Detects strong reflection peaks in each antenna trace.
Fits the hyperbola equation to those detected points.
Estimates depth, target position, and velocity.
The key equation is:
The fitted parameter is the estimated depth.

## Slide 4
B-scan interpretation methodology
The objective of the B-scan interpretation stage is to extract meaningful subsurface information from the generated or measured B-scan image.
Specifically, the methodology aims to estimate:
buried object depth
buried object lateral position
propagation velocity
potential layer boundaries
from the observed hyperbolic signatures.
B-Scan Image
↓
Preprocessing
↓
Hyperbola Detection
↓
Feature Extraction
↓
Hyperbola Fitting
↓
Depth Estimation
↓
Target Localization
Overall Workflow